## Slide 1: A Yang Data Model for ACTN VN Operation
draft-lee-teas-actn-vn-yang-03
Young Lee, Huawei
Dhruv Dhody, Huawei
Daniele Ceccarelli, Ericsson
Takuya Miyasaka, KDDI
Peter Park, KT
Bin Yeong Yoon, ETRI

## Slide 2: Introduction
A Yang Data Model for ACTN VN operations
This is for CMI i.e. CNC – MDSC Interface
  Maps to Customer Service Model
Support for VN views
  As set of E2E tunnels (VN-Member)
  As abstract topology
Support for Access Point (AP) as per the ACTN framework
MDSC translates and maps the VN request into specific network centric-models
  e.g., TE-tunnels [TE-Tunnel], TE-topology [TE-TOPO], etc. and its augmented models
  Coordinate the multi-domain network operations with PNCs.

## Slide 3: Why?
Virtual Network groups multiple E2E tunnels as a VN.
  VN is a unit for concurrency.
  TE-tunnel model deals each VN member as a separate entity, so it loses concurrent allocation of TE resources. TE-tunnel model is a sequential provisioning approach.
It is easier for some customers to work on VN level (Network slice) rather than individual TE tunnels.
ACTN VN supports multi-source and multi-destination use-case.
ACTN VN supports VN compute (pre-instantiation mode) for the whole VN.
There are certain advantages to keep a set of TE-tunnels as one VN unit for applying policy, reroute, protection, restoration, etc. rather than treating each TE-tunnel as individual unit.

## Slide 4: Updates in this version
Reference to TE-Topology’s TP for the ACTN’s AP
Bandwidth
src-tp-id? binary
dst-tp-id? binary
network-ref? -> /nw:networks/network/network-id
Reference to the abstract te topology
bandwidth? tet:te-bandwidth
Added Justifications for this Yang Model

## Slide 5: ACTN VN Yang
List of AP
List of VN
  VN-member list
  Support for multi-src and multi-dest
  Objective Functions
  Metrics
    Limit
    Optimizations
  Other attributes

## Slide 6: ACTN VN Yang
RPC: VN-Compute
  Pre-Instantiation
  Input
    VN-Members with source, destinations
    OF and metric etc
  output
    VN

## Slide 7: NEXT Steps
Continue to enhance the VN Model to meet all requirements of ACTN
  VN-Compute RPC output can be enhanced
Keep align with all ACTN documents including [Info-Model]
Comments?
WG adoption!

## Slide 8: Thank You!