## Slide 1: YANG models for ACTN TE Performance Monitoring Telemetry and Network Autonomics
draft-lee-teas-actn-pm-telemetry-autonomics-00
Young Lee | Huawei
Dhruv Dhody | 
Satish K | 
Ricard Vilalta | CTTC
Daniel King | Lancaster University
Daniele Ceccarelli | Ericsson

## Slide 2: Introduction
YANG data models that describe
  Key Performance Indicator (KPI) telemetry
  Network autonomics for TE-tunnels and ACTN VNs.
[I-D.xu-actn-perf-dynamic-service-control-03]
  Performance Monitoring
  Dynamic control in ACTN – creation, modification, optimization etc.
  Monitor Network Traffic, Detects traffic imbalance, Initiate optimization!
  Measure customer SLA, take dynamic action to make sure you meet them at all times
  Scalability of Performance data
Support for
  Performance telemetry data
  Scaling Intent

## Slide 3: Yang Model Relationships
TE Tunnel
TE KPI Telemetry
Augments
ACTN VN
ACTN TE Telemetry
Augments
TE KPI Telemetry model provides the TE tunnel level performance monitoring.
Augment the TE tunnel State with performance attributes
  Use the notification subscription mechanism to subscribe to telemetry
Scaling Intent configurations for auto scaling in/out based on the performance monitored attributes
ACTN TE KPI Telemetry model provides the VN level aggregated performance monitoring.
Augment the VN state as well as individual VN-member state with performance attributes.
  Use notification subscription
Scaling Intent configurations at the VN level to reach to the monitored performance KPI
Allow configuration of aggregation mechanism from the lower level telemetry details (max, mean etc.)
  From VN-Member to VN
  From per-domain tunnel to E2E VN-Member

## Slide 4: TE KPI Telemetry Yang Model
Telemetry Data
  Delay, Delay-Variation, Packet-Loss, Bandwidth etc
Scaling Intent
  Scale-In
  Scale-Out
  Conditions

## Slide 5: ACTN TE Telemetry Yang Model
VN Level
  Telemetry Data
    Delay, Delay-Variation, Packet-Loss, Bandwidth etc
  The aggregation grouping operation
    Min, Max, Mean, Standard Deviation, Sum etc
  Scaling Intent
    Scale-In
    Scale-Out
    Conditions

## Slide 6: ACTN TE Telemetry Yang Model
VN-Member Level
  Telemetry Data
    Delay, Delay-Variation, Packet-Loss, Bandwidth etc
  The aggregation grouping operation
    Min, Max, Mean, Standard Deviation, Sum etc

## Slide 7: ACTN TE Telemetry Yang Model
VN-Level Configuration
  Scaling
    Scale-In, Scale-Out, Conditions
  Grouping-Op
    Min, Max, Mean, Standard Deviation, Sum etc.
VN-Member Level Configuration
  Grouping-Op
    Min, Max, Mean, Standard Deviation, Sum etc.

## Slide 8: Telemetry Subscription
Via the Notification Subscription / Yang-Push mechanism
  Subscribe notifications on a per client basis.
  Specify sub-tree filters or xpath filters so that only interested contents will be sent.
  Specify either periodic or on-demand notifications.

## Slide 9: Interactions
MDSC
CNC
CNC configure the grouping-operation for delay and bandwidth utilization.
CNC subscribes to the VN level telemetry for delay and bandwidth utilization on a periodic basis
MDSC receives the VN telemetry data
VN-1
VN Bandwidth Utilization as X (Minimum across VN-Members)
VN Delay as Y (Maximum across VN-Members)

## Slide 10: Next Steps
Is this Yang Model useful?
Should we have telemetry and scaling in the same model?
Continue to enhance the model…
Comments welcome!