## Slide 1: Network Artificial Intelligence (NAI)
draft-zheng-opsawg-network-ai-usecases
draft-li-rtgwg-network-ai-arch
Yi Zheng, China Unicom
Zhenbin Li, Jinhui Zhang, Xu Shiping, Dhruv Dhody, Huawei

## Slide 2: Introduction
Explore how Artificial Intelligence (AI) and Machine Learning (ML) can be applied to the network use-cases.
As networks get more and more dynamic & complex, there are new challenges to network management and optimization
  Can NAI help?
What role does a central controller / SDN can play?
  Use Intelligence to drive the controller and implement the recommendations and decisions made by the AI.
This use-case document discusses how the Network Artificial Intelligence (NAI) is able to applied in various possible use-cases.

## Slide 3: Key Functions
Telemetry and Historical Data
Machine Learning
Closed Loop Control
Via SDN
Analytics
Detection, Prescription, Prediction
Build a Network Telemetry Analytics (NTA) engine, usually collocated with a central controller.
E2E deployment may involve multiple NTA engines coordinating with each other similar to the controllers.

## Slide 4: Enhance Path Computation and Traffic Engineering
PCE has access to TEDB + LSP-DB
Adding history records of the changes in LSP-DB and TEDB for analytics
Adding Network Telemetry as well as real-time analytics of traffic monitoring, statistics etc.
  PCE reroute/re-optimize using the historical trend and predications from NAI
  PCE could handle the changes in bandwidth utilization and other performance monitoring data for predicted traffic congestion avoidance.
Build intelligent context
  What is the LSP/Path used for?
PCE
NTA
Historical Record &
Telemetry
Network Telemetry
PCEP, BGP-LS etc

## Slide 5: Route Monitoring and Analytics
BMP can be used to monitor the BGP peer.
The controller can monitor the BGP status and routing information of the routers using BMP.
Historical records of changes can be maintained in the NTA for analytics
Telemetry information can be added.
Possible use-cases
  BGP Route Leaks
  BGP Hijacks -
  Traffic Analytics and intelligent Traffic Engineering
Intelligent detection via anomaly detection!
ISP1
ISP2
Controller
NTA

## Slide 6: Multilayer Fault Detection in NFV
Telemetry data from all layers
  CPU performance, memory usage, interface bandwidth and other KPI indicators can be monitored.
  At the same time resource occupancy and the life cycle of NVF software process can also be monitored.
Historical records – correlate and categorize.
Through the NAI, the relevant statistical data in multiple levels can be analyzed and the models can be setup to locate the root cause for the possible fault in the multi-layer environment.
Intelligent Health Diagnostic
Compute
Network
Storage
Virtualization Layer
Compute
Network
Storage
VNF
VNF
VNF
MANO
NTA

## Slide 7: Smart SFC
Network Telemetry - delay, jitter, packet loss from the network
Service telemetry - CPU/memory usage utilizations from the SFs
Via sFLOW/gRPC protocol and stored as historical records
The analytics component in NTA can build models to predict the impact on various Service Function Paths due to network events, traffic and state of the SFPs and instruct the SFC controller to take necessary actions
The SFC controller can calculate new paths/reroute the SFC path to avoid congested Ports/SFFs or overloaded SFs
SFC
Controller
NTA
Telemetry

## Slide 8: Architectural Considerations
Placement of NTA
  Collocated with Controller
  Integrated with controller
Handling of multi-domain controllers
  Analytics closer to the source is better!
  Hierarchy (like ACTN…)
Building Blocks
  Telemetry Collector (Data Collector)
  Data Movement
  Analytics – real time or batch
  ML Models
  Visualization
  Closed Loop Interactions

## Slide 9: Next Steps
Are these the right set of use-case to explore AI/ML in the networks?
  Do you have other use-cases?
  Is it useful to document them and discuss?
  Please suggest and collaborate!
What are the architectural considerations, that should be considered?
  Are there any protocol considerations?
Build prototypes, reuse various possible open-source.
  Hopefully in a future Hackathon!

## Slide 10
Thank You!