## Slide 1: Stateful H-PCE & ACTN
Hierarchical Stateful PCE | draft-dhodylee-pce-stateful-hpce-03
Applicability of PCE for ACTN | draft-dhody-pce-applicability-actn-02
PCEP Extensions for Establishing Relationships Between Sets of LSPs and VNs | draft-leedhody-pce-vn-association-02
Dhruv Dhody, Young Lee, Daniele Ceccarelli, Jongyoon Shin, Dan King, Oscar Gonzalez de Dios, Xian Zhang | 

## Slide 2: Documents Relationship
PCEP-LS
draft-dhodylee-pce-pcep-ls-07
Stateful H-PCE
draft-dhodylee-pce-stateful-hpce
VN Association
draft-leedhody-pce-vn-association-02
Others
draft-litkowski-pce-state-sync
Applicability of PCE for ACTN
draft-dhody-pce-applicability-actn-02
This Presentation
ACTN Specific

## Slide 3: Stateful H-PCE
H-PCE + Stateful PCE
Hierarchy of Stateful PCE
-00 version was discussed in the IETF 95 (BA)
Marked ‘Informational’
Parent Stateful PCE
Child Stateful PCE
with per domain TEDB and LSPDB
Maintain the domain topology map
and LSPDB

## Slide 4: Stateful H-PCE – Changes since -00
Clarification on the recursive nature of Stateful PCE constructs
  Delegation, Reports, Updates
Capability advertisements
  H-PCE capability TLV [I-D.ietf-pce-hierarchy-extensions]
  Stateful PCE capability TLV [I-D.ietf-pce-stateful-pce]
State sync procedures and update
  as per [I-D.litkowski-pce-state-sync]
Scalability Consideration
  only report necessary LSPs to the parent PCE
Security & Manageability Considerations

## Slide 5: VN Association
ACTN describes various Virtual Network (VN) operations.
  Associating a set of LSPs with a VN "construct" to facilitate VN operations.
  This ‘association’ allows the PCEs to identify which LSPs belong to a certain VN.
  The PCE could then use this association to optimize all LSPs belonging to the VN together.
  The PCE could further take VN specific actions on the LSPs such as relaxation of constraints, policy actions, setting default behavior etc.
Using ASSOCIATION object [I-D.ietf-pce-association-group]
-00 version presented in IETF 95 (BA)

## Slide 6: VN Association – Changes since -00
Path Computation
  When computing path for a LSP, the impact of this LSP, on the other LSPs belonging to the same VN is useful to analyze.
  The aim would be optimize overall VN and all LSPs, rather than a single LSP.
  Apply optimization criteria for all LSP in the group.
Path Re-Optimization
  The child or Parent PCE can use advanced path computation algorithm and optimization technique that consider all the LSPs belonging to a VN/customer and optimize them all together.
Usefulness of this relationship between parent and child PCE for ACTN VN operations
Support for VENDOR-INFORMATION-TLV
Security & Manageability Considerations

## Slide 7: Applicability of PCE for ACTN
ACTN – Abstraction and Control of TE networks
Four Functions in ACTN
  Multi domain coordination function
  Virtualization/Abstraction function
  Customer mapping/translation function
  Virtual service coordination function
We list all ways PCEP could be used
MDSC
MDSC
MDSC
MDSC
PNC
PNC
PNC
PNC
PNC
CNC
CNC
CNC
CMI
MMI
MPI
PCEP
CNC | Customer Network Controller
MDSC | Multi-Domain Service Coordinator
PNC | Physical Network Controller
CMI | CNC-MDSC Interface
MMI | MDSC-MDSC Interface
MPI | MDSC-PNC Interface

## Slide 8: Architectural Considerations
Multi domain coordination
MDSC oversees different domains and build an E2E abstracted topology and coordinate E2E path/service provisioning.
An abstracted view of underlying network resources of each domain to form an E2E network topology.
Customer mapping/translation
Map customer VN requirements into network provisioning requests that are serviced by the PNC
Virtual service coordination
Seamless virtual network operations for each customer
Virtualization/Abstraction
Includes customer’s view of network slice
Stateful H-PCE
PCEP-LS
VN-Association
Stateful PCE with initiation
H-PCE
With support for abstract topology
Virtual Network
Associate set of LSPs to a VN
Per-domain stitched LSP

## Slide 9: Applicability of PCE for ACTN – Changes since -00
Clarification that PCEP doesn’t need to be used for all functions in all deployments
Clarifications around ACTN functions and other PCEP extensions such as
  [I-D.litkowski-pce-state-sync]
  [I-D.ietf-pce-association-policy]
  [I-D.lee-teas-actn-abstraction]
Relationship to PCE based central control

## Slide 10: How to progress these documents?
Independent
Stateful H-PCE
PCEP-LS
ACTN Specific
ACTN Applicability
ACTN-VN association
These functions are hacked on, implemented, showcased during past IETF
Implementation reports for some, shared on the list.
All comments so far are handled
More reviews are always welcome.
WG Adoption
In a particular order?
PCEP-LS, Stateful H-PCE, VN-Association etc

## Slide 11
Thank You!